## Slide 1: 计算思维与系统设计基础
Weekly report
Week 2
第四组
田卓钰 孔德嘉 南佳凡

## Slide 2: Project2 Boolean Arithmetic
by 第四组 田卓钰

## Slide 3: Add16
题目理解：完成两个16位数的相加（不处理溢出）。

## Slide 4: 思路
16位加法器，则输入应当是a[16],b[16],out[16]，这是header的内容。
第一排，只有最右边两位相加，a[0],b[0],只需要a,b两个管脚，所以用Half-Adder，当然a=a[0],b=b[0],sum（表示最右边一位）=out(0)(对下一次运算没有影响了），carry(当前运算最左边一位，可能进位，所以对下次结果有影响，会是下一次运算的一个输入）=carry0(表示当前位数，当然是0位）
从第二排开始，就是不断重复，所以仅介绍第二排。

## Slide 5
第一次运算后，关乎进位的carry需要用上，再加上a[1],b[1],三个输入管脚，需要用 Full-Adder，a,b,c分别对应a[1],b[1],carry0,sum=out[1](此次这一位运算结果），carry=carry1)
一直到最后一位重复这个操作，无需赘言。

## Slide 6: Add16的HDL:
CHIP Add16 {
IN a[16], b[16];
OUT out[16];
PARTS:
Half-Adder(a=a[0], b=b[0], sum=out[0], Carry=carry0);
Full-Adder(a=a[1], b=b[1], c=carry0, sum=out[1], carry=carry1);
Full-Adder(a=a[2], b=b[2], c=carry1, sum=out[2], carry=carry2);
Full-Adder(a=a[3], b=b[3], c=carry2, sum=out[3], carry=carry3);
Full-Adder(a=a[4], b=b[4], c=carry3, sum=out[4], carry=carry4);
Full-Adder(a=a[5], b=b[5], c=carry4, sum=out[5], carry=carry5);

## Slide 7
Full-Adder(a=a[6], b=b[6], c=carry5, sum=out[6], carry=carry6);
Full-Adder(a=a[7], b=b[7], c=carry6, sum=out[7], carry=carry7);
Full-Adder(a=a[8], b=b[8], c=carry7, sum=out[8], carry=carry8);
Full-Adder(a=a[9], b=b[9], c=carry8, sum=out[9], carry=carry9);
Full-Adder(a=a[10], b=b[10], c=carry9, sum=out[10], carry=carry10);
Full-Adder(a=a[11], b=b[11], c=carry10, sum=out[11], carry=carry11);
Full-Adder(a=a[12], b=b[12], c=carry11, sum=out[12], carry=carry12);
Full-Adder(a=a[13], b=b[13], c=carry12, sum=out[13], carry=carry13);
Full-Adder(a=a[14], b=b[14], c=carry13, sum=out[14], carry=carry14);
Full-Adder(a=a[15], b=b[15], c=carry14, sum=out[15], carry=carry15);
}

## Slide 8
ALU ALU是算术逻辑单元的缩写，简言之，它有两个16位输入管脚，6个控制位（下一页介绍），这6个控制位可以构成2的6次方=64个不同函数。这些控制位的功能包括：预设x，y的输入，选择+还是And运算,对结果是否取反。还有3个输出位，用来输出结果，显示结果是否为0，以及是否小于0.

## Slide 9
alu的输入是十六位的x,y，六位控制台：
zx:对x取0
zy:对y取0
nx:对x按位取反（如果是0，按位取反后是-1，当然，编码是-1的补码，即2的n方-x（绝对值））
ny:亦然
f:用来选择是+还是and，为0就是and,否则是+
no:对结果按位取反。
输出：out:函数运算后结果
zr:out为0时取1，否则取0
ng:out为负取1，否则取0

## Slide 10
Parts: （按照控制台顺序） 根据zx的输入决定x是否取0，因此使用Mux,语句是Mux(a=x,b=False(也就是0),sel=zx,out=x0（内部管脚可以自己命名)
决定是否取反，需要两句，第一句用Not取反得到一个结果，第二句决定是采用Not后的结果，还是原结果，这由输入的nx值确定，所以又是一个Mux。
Y的语句和x没有什么不同，无需赘言。
现在x,y的输入已经决定好了，下一步是选择+还是And,这和决定x，y是否取反的方法一样的，先用Add，And语句各得出一个结果，再用Mux决定选取哪一个。

## Slide 11
下一步是输出结果，仍是同样的方式，取反得出一个结果，用Mux决定选择取反后的结果，还是未取反的结果。
还要输入zr和ng。
对zr，需要先判断out是否为0，方法很巧妙，用or语句确定（好吧，你们一定觉得是套路），下一步，如出一辙是用Mux。
对ng，需判断是否out<0,这是有Isneg16(Is negative?16位），如果是负数，输出1，否则输出0，根据这个结果用Mux。得出ng值。

## Slide 12
CHIP ALU {
IN
x[16], y[16],zx,nx, zy, ny,f,no;
OUT
out[16],zr,ng;
PARTS
Mux16(a=x, b=false, sel=zx, out=xval1); Not16(in=xval1, out=notxval);
Mux16(a=xval1, b=notxval, sel=nx, out=xval); Mux16(a=y, b=false, sel=zy, out=yval1);
Not16(in=yval1, out=notyval);
Mux16(a=yval1, b=notyval, sel=ny, out=yval);

## Slide 13
PARTS:
Add16(a=xval, b=yval, out=sum);
And16(a=xval, b=yval, out=and);
Mux16(a=and, b=sum, sel=f, out=out1);
Not16(in=out1, out=notout);
Mux16(a=out1, b=notout, sel=no, out=out2);
Or16Way(in=out2, out=outnonzero);
Mux(a=true, b=false, sel=outnonzero, out=zr);
IsNeg16(in=out2, out=neg);
Mux(a=false, b=true, sel=neg, out=ng);
Or16(a=out2, b=false, out=out);

## Slide 14
Thanks for your listening.

## Slide 15: Chapter 3 Sequential Logic
时序逻辑
工物40 孔德嘉
2017年10月

## Slide 16
Combinational Logic
Sequential Logic

## Slide 17
Combinational Logic
Sequential Logic
Maintain state

## Slide 18
Combinational Logic
Sequential Logic
Maintain state
data flip-flop
D触发器
out(t)=in(t-1)

## Slide 19
DFF(built in)
Register
Memory
Counter
1-Bit Register (Bit)
w-Bit Register
8-Register Memory (RAM8)
RAM64
RAM512
RAM4K
RAM16K

## Slide 20
1-Bit Register (Bit)

## Slide 21
1-Bit Register (Bit)

## Slide 22
1-Bit Register (Bit)

## Slide 24
谢谢！

## Slide 25: Project 4
Machine Language Programming
南佳凡 自64

## Slide 26: 知识内容
Assembly Language
Assembler
CPUEmulator

## Slide 27: 题目
1.mult
Multiplies R0 and R1 and stores the result in R2.
(R0, R1, R2 refer to RAM[0], RAM[1], and RAM[3], respectively.)

## Slide 28: MULT
输入：R0 , R1
过程 : 循环，R1个R0相加
输出 : R2
效果 : R2=R0*R1

## Slide 31
谢谢！

## Slide 32
Wiki活跃度

## Slide 33
Wiki活跃度

## Slide 34
GitHub活跃度